## Slide 1: The Controlled-Autonomous Rover
Ben Brown, Ganquan Wen, Zisen Zhou, Nicholas Arnold, and Mohammed Uddin

## Slide 2: Goal and Motivation
Implement a “RC” Car using an FPGA with distinct modes
  Controlled
  Autonomous
Add unique peripherals
  Bluetooth for controls & live stats
  Ultrasonic Sensor/Light Sensor to detect environment
  Motors to drive the rover
Main Features
  Autonomous mode! Implement a decision making vehicle based on feedback from sensors
  Using Verilog and the FPGA to handle interactions between different peripherals
Notes: MO

## Slide 3: High Level Functionality
Notes: Ben

## Slide 4: Specification Overview
Motors
  Take a barebones RC car base, and control the motor with varying speeds
  Requirements: receive signals from either bluetooth module OR sensor feedback and drive the car
Bluetooth
  Implement bluetooth controls via UART
  Requirements: FPGA receives serial data through UART rx, parses this data, and produces accurate control for the motor
Sensors
  Implement sensors Ultrasonic distance sensors to detect obstacles
  Requirements: Send accurate and real time signals to FPGA, design an algorithm to decide how the steering and movement should behave autonomously
Notes: MO

## Slide 5: Detailed Functionality - Motors
2 DC Motors
  Rear motor for forward/backward and speed
  Front motor for turning
3 different speeds can be selected in manual mode
  65%, 80% and 95% duty cycle respectively
Autonomous mode defaults to slowest speed
Different speeds implemented with pulse width modulation (PWM) of rear motor
Notes: Ben

## Slide 6: Motor Driver L293D
4 tri-states
  2 Enable pins
Low current logic level signals in
Output pins output up to 0.6A each
PWM implemented by disabling and enabling Rear+ and Rear- outputs
-
-
Input
Input
Input
Input
Input
Output
Output
Output
Output
Notes: Ben

## Slide 7: Detailed Functionality -Adafruit Bluetooth
BT button presses are sent as serial ASCII over the air then on the TX pin
Also can type in ‘a’ ‘c’ or ‘s’ for auto/ctrl/stop
Each Button Consists of 5 Bytes
  Last is Cyclic Redundancy Check
UART Rx converts serial to Bytes
Parser reads them in & translates into button val
Controller listens to button & outputs control signals to motor controller for speed, mode, and directions
Notes: NICK

## Slide 8: Bluetooth Rx Block Diagram
Notes: NICK

## Slide 9: Command Parser
Notes: NICK

## Slide 10: Controller
Notes: NICK

## Slide 11: Detailed Functionality - Sensors & Autonomous
Able to get accurate and stable distances from sensors.
  Measure distance every 0.1 second
  Update design from last version to be stabler
  Display the distance of one of the front sensor on seven segments display
Four sensors work at the same time without affecting others.
  2 in the front
  2 on left and right
  Use one signal to trigger all ultrasonic sensors to save I/O ports
The car can run autonomously according to the results get from the sensors.
  FSM to control the car
  Coordinate with motor drivers to make car move around safely
Notes: Jason

## Slide 12: Sensors Block Diagrams
Echo Receiver
Start sending ultrasound (Set Echo to 5v)
Receive returned ultrasound(Set Echo to 0v)
Echo
Trig
10us
t
t
V
V
Ultrasonic Transmitter
Notes: Jason

## Slide 13: Autonomous Mode Diagram
The distances of going backward or turning are decided by the time staying at the corresponding state.
Notes: Gan

## Slide 14: Verilog: BT Controller

## Slide 15: Successes
Varying motor speed based on user input
Serial Communication between Phone, FPGA, and motor drivers
Feedback from sensors converted into control signals
Sensors and solderable breadboard mounted on car
Overall: Timing and interaction between the different peripherals and the FPGA is smooth

## Slide 16: Videos
Manual Control
Autonomous Control
Notes: Gan for autonomous

## Slide 17: Failures and Obstacles
Bluetooth
  Displaying sensor data (distance from objects) back on to the interface
Sensor
  Did not implement the light sensors
Motors
  Turning left is sometimes not as sharp as turning right
  Turning in general is not as responsive when rear motors are at maximum speed

## Slide 18: Tasks to be Done
Mount Microzed on board and connect inputs and outputs
Program Microzed to boot preprogrammed bitstream when battery powered
Transmit object distances to Phone App
More testing to fine tune parameters for autonomous mode
Notes: BEN

## Slide 19: Design Tradeoff Discussion
Microzed over Zedboard
  Zedboard requires 12V, 5A power supply
  Microzed only requires 5V, 2.5A, powered by microUSB
  Smaller and easier to mount, lighter weight
Sensors
  More sensors can let the car detect better, but it will use more I/O and add more weights.
  Light sensors are cool, but gimmicky (simple leds don’t serve a real purpose or function in this case)

## Slide 20: Attribution of Work
Mo - Bluetooth Parsing, Control structure, Feedback Data, App
Nick - Bluetooth Parsing, Control structure, Feedback Data, App
Gan - Sensors and autonomous mode
Zisen - Sensors and autonomous mode
Ben - Motor controller, physical mounting/wiring, and integration of control modes