## Slide 1: FPGAng’s Controlled-Autonomous Rover
Ben Brown
Nicholas Arnold
Mohammed Uddin
Ganquan Wen
Zisen (Jason) Zhou

## Slide 2: Overall Goals
Implement a “RC” Car using an FPGA with distinct modes
  Controlled
  Autonomous
Add unique peripherals
  Bluetooth for controls & live stats
  Ultrasonic Sensor/Light Sensor to detect environment
  Motors to drive the rover
Main Features
  Autonomous mode! Implement a decision making vehicle based on feedback from sensors
  Using Verilog and the FPGA to handle interactions between different peripherals

## Slide 3: BLock Diagram of System

## Slide 4: Motor Controls (Ben)
What is done?
  Variable speed motor controller module
  Successfully interfaced RC car motors with Nexsys 3 board and L293D motor driver (video)
What is being worked on now?
  Fine tuning minimum and maximum speeds based on weight of Zedboard on top of car
  Fine tuning PWM frequency to avoid motor whining
  Planning out wiring from FPGA to L293D, motors, and battery pack
What is yet to be started?
  Interfacing motor driver and motors with Zedboard
  Take inputs from Bluetooth
  Physical mount for L293D chip, sensors, and Zedboard

## Slide 5: Video of Motor Controls

## Slide 6: Bluetooth Control and Android App (Nick and Mo)
What is completed?
  Basic Android App Interface
  Bluetooth connectivity
    Sending signals from phone to Adafruit Bluetooth chip
    F,B,L,R buttons for directions + slider for speed
What is being worked on right now?
  Connecting bluetooth module to the Zedboard via UART (currently testing on breadboard)
  Test data rate, and clocking it appropriately (send signals fast enough / appropriate to communicate)
  Modules to translate signal bytes into movement parameters
Down the road
  Test controls with Ben’s modules and our modules on the Zedboard with verilog
  Switch states between autonomous and controlled, tune decision making logic
  Modules to take speed & sensor stats, communicate them to display on the phone

## Slide 7: Sensors - Ultrasonic and Light (Gan and Jason)
What is completed?
  Ultrasonic sensor can measure distance to the block in front of it.
  The result can be displayed on the 7-segment. The accuracy is good.
What is being worked on right now?
  Sometimes it gets incorrect result while the distance is changing. (We will see that on the video) We are trying to find out the cause of that and fix it.
  Algorithm and priority of of five sensors.
Down the road
  Implement five sonic sensors working at the same time.
  The light sensor.
  Test controls with other module

## Slide 8: Videos of Testing Sensor

## Slide 9: Things going well
Motor/Controls
  Both the rear motor and motors for turning are simple DC motors, easy to drive and control
Bluetooth connectivity
  Android Application
  Sending strings/data to BT chip from phone
  Data stream (send four 1-bit outputs for direction and either a 7-bit output for “levels” of speed)
Sensors
  Testing ultrasonic sensor with 7-segment display

## Slide 10: Things to improve on
Motor/Controls
  Speed adjustments as programmed now might be too fine
  Physical mounting may be too heavy
Bluetooth connectivity
  Making sense of the data stream received from Bluetooth Module onto board’s UART
  Converting the information received from the Bluetooth module to the board to something that can drive the car
Sensors
  The stability of the distance measured
  Making decisions based on the sensor feedback (autonomous mode)

## Slide 11: Timeline
Feb 15th March 1st March 15th March 22nd April 1st April 15th Apr. 26th May 1st
First Presentation
Demo
Materials Obtained
Motors Steering Controls Implemented
Final Presentation
Order Parts
Functioning App with Bluetooth
Integration and testing phase
Controls Code
Autonomous Mode
& Sensors

## Slide 12: Bill of Materials
$97.65

## Slide 13
Give us feedback!
Questions?